AGY:	Department of Health and Environmental Control 61

FII:	6

FIV:	23

PRD:	19981023

EFD:	19990625

EXD:	19990530

REG:	2351

PRI:	10

PRV:	22

COM:	Agriculture and Natural Resources Committee 1 SANR

Agriculture, Natural Resources and Environmental Affairs Committee 20 HANR

RES:	4073

STA:	Final

AUT:	48-1-10 et seq.;44-55-10 et seq.

SUB:	Individual Residential Well and Irrigation Well Permitting

HST: 2351

BY	DATE	ACTION DESCRIPTION	COM	ISS/VOL	EXP DATE	R. NUM

__	________	_____________________________	_______	________	__________	_______

-	19981023	Proposed Reg Published in SR		10/22

-	19990112	Received by Lt. Gov & Speaker			19990511

H	19990112	Referred to Committee 	HANR 20

S	19990113	Referred to Committee 	SANR 1

H	19990506	Committee Request Withdrawal	HANR20

120 Day Period Tolled

-	19990510	Withdrawn and Resubmitted			19990530

H	19990511	Resolution Intro to Approv	HANR 20			H4073

-	19990530	Approved by:  Expiration Date		23/6

TXT:

Resubmitted May 10, 1999

Document No. 2351

DEPARTMENT OF HEALTH AND ENVIRONMENTAL CONTROL

CHAPTER 61

Statutory Authority: 1976 Code Sections 48-1-10 et seq. and 44-55-10 et seq.

Synopsis:

The South Carolina Department of Health and Environmental Control has concluded that the improper installation of individual residential wells and irrigation wells is endangering public health and the quality of groundwater in this State.  Regulation 61-44, Individual Residential Well and Irrigation Well Permitting,  provides for establishing a permitting procedure, a permitting fee, inspections, and enforcement.  (See Statement of Need and Reasonableness herein.)

Sections A, B, and C address the purpose of the regulation, its applicability requirements and definitions.

Section D addresses Notice Of Intent, Permitting, and Approval procedures.

Section E provides for emergency well replacement.

Section F provides for a permit fee to be established in Regulation 61-30, Environmental Protection Fees.

Section G adopts by reference  Regulation 61-71, Well Standards.

Sections H and I address enforcement and penalties for violations.

Instructions:  Add new Regulation 61-44, Individual Residential Well and Irrigation Well Permitting, to Chapter 61 regulations.

Text:

61-44.  INDIVIDUAL RESIDENTIAL WELL AND IRRIGATION WELL PERMITTING

Table of Contents:

A.	Purpose and Scope.

B.	Definitions.

C.	General.

D.	Notice of Intent, Permit, and Approval.

E.	Emergency Well Replacement.

F.	General Permit Fee.

G.	Reference.

H.	Enforcement.

I.	Violations, Penalties.

J.	Severability.

A.	PURPOSE AND SCOPE.

1.	This regulation, promulgated pursuant to the  authority  of  the Pollution Control Act, Section 48-1-10 et seq.,  and the  Safe Drinking Water Act, Section 44-55-10 et seq., 1976 S.C. Code of Laws, establishes a system and rules for managing and protecting the quality of South Carolinas groundwater, drinking water, and for protection of public health.

2.	The South Carolina Department of Health and Environmental Control has concluded that the improper installation of individual residential wells and irrigation wells are endangering public health and the quality of groundwater in this state and therefore finds the need for regulation to govern installation of such wells.

B.	DEFINITIONS.   The definition of any word or phrase employed in this regulation shall be the same as given in the Well Standards, R.61-71,  Pollution Control Act, 48-1-10 et seq.,  and the  Safe Drinking Water Act, Section 44-55-10 et seq., 1976 S.C. Code of Laws.   Words or phrases which are not defined in the Acts or Regulations are defined as follows:

1.	Agent- a person acting on behalf of an owner, subject to the control of the owner, who acts in such a manner as to affect the legal relationships of the owner with third parties.

2.	General Permit - a permit for the construction of individual residential wells or irrigation wells issued under this regulation authorizing a category of well construction activities within the state.

3.	Human Consumption - water used for drinking, bathing, cooking, dishwashing and maintaining oral hygiene, or other similar uses.

4.	Individual Residential Well - a potable water well intended to produce water for human consumption at a single residence or family.

5.	Irrigation Well  -  a well intended to produce water for uses other than human consumption, to include, but not be limited to, lawn and landscape watering and agricultural uses.

6.	Owner - a property owner where the well is to be constructed.

7.	Replacement Well - a well being constructed to take the place of an existing individual residential well or irrigation well that is being taken out of service.

8.	Residence - legal residence; the permanent, fixed place of abode which a person intends to be his residence and to which he intends to return.

9.	Well driller - an individual, corporation, partnership, association, political subdivision, or public agency of this State who is licensed with the S.C. Department of Labor, Licensing, and Regulation for constructing wells and is in immediate supervision of, and responsible for, the construction, development, drilling, testing, maintenance, repair, or abandonment of any well as defined by this regulation.   This term shall include owners constructing or abandoning wells on their own property for their own personal use only, except that such owners are not required to be licensed by the Department of Labor, Licensing, and Regulation for constructing wells and are not subject to the bonding requirements of subsection (C)(4) of this regulation.

C.	GENERAL.

1.	Individual residential wells and irrigation wells shall be constructed or abandoned by well drillers who are licensed for such purposes by the S.C. Department of Labor, Licensing, and Regulation.  The licensing required by the subsection does not apply to owners constructing or abandoning wells on their own property for their own personal use only.

2.	All individual residential wells and irrigation wells shall be constructed or abandoned in accordance with this regulation, Regulation 61-71, Well Standards, and all other applicable laws, regulations, and standards.

3.	The Department must conduct necessary inspections, to the maximum extent as resources allow,  to ensure compliance with the provisions of this regulation.  The owner shall grant access to the well construction site to the Department at reasonable times for the purpose of conducting such inspections.  The inspection program will primarily be conducted by Department personnel located in the District Environmental Quality Control offices. Inspections shall be conducted at the time of construction when possible.  The purpose of inspections is to determine compliance with the Well Standards R.61-71 and this regulation.  The inspections shall include, at a minimum, determining: 1) proof of coverage under the general permit, 2) compliance with siting requirements, 3) the presence or absence of an adequate grout seal and compliance with other critical construction standards outlined in R.61-71, and 4) eventual timely submittal of the well record form.  Violations of the cited regulations noted during the inspection shall result in enforcement action in accordance with established Department procedures.  The Department shall develop an inspection manual which outlines the complete inspection process for Department personnel in accordance with the requirements of this regulation and the Well Standards R.61-71.   Interested parties may provide input into development and annual updating of the inspection manual.   After one years  training and experience, each district well inspector shall conduct a minimum of 200 inspections annually of individual residential or irrigation wells with a Department  goal to inspect a majority of wells constructed under this regulation.  Owners shall be provided a copy of the Departments  inspection results.

4.	The Department shall prepare an annual report detailing activities funded by individual residential well and irrigation well fees including the number of wells issued coverage under the general permit, number of inspections, inspection results, fees collected, and number of enforcement actions.  This report shall be submitted to the South Carolina Legislature and the South Carolina Groundwater Association and be available for the general public.

5.	Each well driller must meet bonding requirements as established by the Department of Labor, Licensing, and Regulation.  The Department shall have full access to a well drillers bond to correct a violation of this regulation and/or Regulation 61-71, Well Standards,  where, as part of a Department enforcement action, a well driller is unwilling or unable to take required corrective actions.    The bonding provisions required by the subsection does not apply to owners constructing or abandoning wells on their own property for their own personal use only.

6.	Irrigation wells shall not be permitted at a residence unless another source of potable water serving the residence is proposed or exists.

7.	The Department is authorized to develop a General Permit for individual residential well and irrigation well activities.

8.	This regulation will become effective 60 days after Legislative approval.

D.	NOTICE OF INTENT, PERMIT, AND APPROVAL.

1.	It shall be unlawful to construct an individual residential well, an irrigation well, or a replacement well unless conditions of the general permit issued by the Department have been satisfied for the construction of the proposed well.

2.	It shall be the responsibility of the well driller to ensure that coverage under this general permit to construct an individual residential well,  irrigation well, or replacement well is obtained from the Department prior to construction of the well.

3.	It shall be the responsibility of the well driller to ensure that all wells permitted under this regulation are located and constructed in accordance with all applicable regulations.

4.	  A Notice of Intent (NOI) form provided by the Department, as specified in the general permit, must be submitted to the Department with true and accurate information necessary for determining the location of, and proper construction of, individual residential wells, replacement wells, and  irrigation wells.  The NOI may be submitted by the owner, agent, or well driller.  This information shall include, but may not be limited to, owner name, address, and telephone number, address of the property on which the well is to be installed, proposed date of installation, proposed well location, if the proposed well is a new well or replacement well, and name and license number of the licensed well driller constructing the well.  If any information provided on the NOI changes at the time of well construction, the well driller must contact the Department and provide the correct information.

5.	Upon receipt of a completed NOI, the Department shall accomplish its review and have either the approval, review comments, or denial transmitted to the applicant within 48 hours.  The 48 hour period is calculated from the time and date of receipt of the Notice of Intent excluding weekends and legal state holidays.  If notice is not given to the applicant by the end of the 48 hour period, coverage under the general permit for individual residential wells and irrigation wells will be considered approved.  The well driller shall also give the Department 48 hours prior notice of well installation with the exact date, time, and location of well installation.  This notice can be concurrent with the NOI review period.  The Department shall deny coverage under the general permit when the proposed well would violate Regulation 61-71, Well Standards, the Pollution Control Act, Section 48-1-10 et seq., the  Safe Drinking Water Act, Section 44-55-10 et seq., 1976 S.C. Code of Laws, or licensing requirements established by the S.C. Department of Labor, Licensing, and Regulation.   Nothing in this regulation shall be used to limit construction of individual residential wells or irrigation wells that are constructed in accordance with the applicable regulations cited above.  The  Department inspectors will utilize available resources, such as Department records of  permits for onsite wastewater systems and subdivision application approvals, to help determine compliance with the NOI provisions in this regulation.

6.	Coverage under a general permit issued pursuant to this regulation shall not guarantee that a well will yield water that is of adequate quality and/or quantity for the purposes intended.

7.	The well driller shall have a copy of the Notice of Intent before initiating construction of an irrigation well or individual residential well and shall keep a copy of the Notice of Intent on the drilling site at all times.

E.	EMERGENCY WELL REPLACEMENT.   A well driller may replace an existing individual residential well immediately when an emergency exists.  An emergency is deemed to exist when an existing individual residential well has suddenly been rendered useless or the water quality is not fit for human consumption and a replacement well is needed to provide a potable water supply.  The Notice of Intent and associated fee shall be submitted within 24 hours of well construction.

F.	GENERAL PERMIT FEE.

1.	 Each well driller, owner, or agent applying for a general permit to construct a new or replacement individual residential well or irrigation well shall pay to the Department a fee in accordance with Regulation 61-30, Environmental Protection Fees.

2.	Upon notification of the Department, no permit fee shall be assessed to a well driller, owner, or agent who has replaced, within one year of installation, an  unserviceable or otherwise unsatisfactory individual residential well or irrigation well if the unserviceable or unsatisfactory well is properly abandoned.

3. The fee collected must be returned to the Department for the sole purpose of developing and implementing the Individual Residential Well and Irrigation Well Program, including proposed well construction review, compliance inspections, technical assistance, enforcement, and for providing bacteriological analytical services for new individual residential wells.

G.	REFERENCE.  The definitions and standards established by Regulation 61-71, Well Standards, are herein adopted by reference.

H.	ENFORCEMENT.  For the purpose of enforcing this regulation, an employee or duly authorized representative of the Department may enter at reasonable times the site of well construction on the property of an owner where a permit has been obtained pursuant to this regulation.  The Department, upon receipt of information that a constructed individual residential well or irrigation well may present an unacceptable risk to health of the persons using the well or to the groundwaters of the State, or is in violation of any other applicable statutes or regulations,  will initiate enforcement action against the well driller.

I.	VIOLATIONS; PENALTIES.

1.	Violations of this regulation shall be subject to penalties as provided in  Sections 48-1-320, 44-55-90 and 48-1-330 of the 1976 S.C. Code of Laws.

2.  Whenever the Department finds that a well driller is in violation of a permit, regulation, standard, or requirement under this regulation, the Department, after written notice of violation, may issue an order requiring the well driller  to comply with the permit, regulation, standard, or requirement, or may request the Attorney General to commence an action under this subsection in the appropriate court.  The Department may also assess civil penalties as provided in this section for violations of the provisions of this regulation including any order, permit, regulation, or standard.

3.  A well driller who fails to take appropriate corrective action, after receiving written notice of violation of a provision of this regulation, is liable for civil penalties or criminal prosecution.

4.  A well driller who fails to notify the Department per Section D.5, or fails to obtain coverage under the general permit, after receiving written notice of violation of a provision of this regulation, is liable for civil penalties.

5.  The Department shall have full access to a well drillers bond required by the Department of Labor, Licensing, and Regulation to correct a violation of this regulation and/or Regulation 61-71, Well Standards,  where, as part of a Department enforcement action, a well driller is unwilling or unable to take required corrective actions.

J.	SEVERABILITY.	Should any section, paragraph, sentence, clause,  phrase, or other part of this regulation be declared invalid for any reason, the remainder shall not be affected thereby.

Preliminary Fiscal Impact Statement:

The Department estimates that the State and its political subdivisions will incur no additional financial impact by the promulgation of this regulation.  Cost of implementation will be met by fees imposed by the regulation.

Statement of Need and Reasonableness:

The statement of need and reasonableness was determined by staff analysis pursuant to S. C. Code Section 1-23-115(C)(1)-(3) and (9)-(11):

DESCRIPTION OF REGULATION: New Regulation 61-44,  Individual Residential Well and Irrigation Well Permitting

Purpose:  Regulation 61-44 will help protect the quality of South Carolinas groundwater, drinking water, and public health.   It provides for establishing a permitting procedure, a permitting fee, inspections, and enforcement.

Legal Authority: S.C. Code Sections 48-1-10 et seq., and 44-55-10 et seq.

Plan for implementing:  Upon approval by the General Assembly and publication in the State Register, copies of the regulation will be provided to the regulated community.  A permitting process and inspection program will be established.  The impact to other program areas should be negligible.

DETERMINATION OF NEED AND REASONABLENESS OF THE PROPOSED REGULATION BASED ON ALL FACTORS HEREIN AND EXPECTED BENEFITS: Safe drinking water is essential to public health.  It is also important to economic development and is a basic indicator of the quality of life.  Therefore, protection of drinking water is of critical importance.  Approximately 40% of South Carolinas population uses groundwater as their drinking water source.   The need for this regulation is demonstrated by a series of inspections of individual residential wells, the most recent being in 1997, which revealed that approximately one-third of the wells inspected were not properly constructed.  Substandard well construction poses a risk to the health of the residents using that well and a risk of contamination being introduced to the aquifer(s) penetrated by the well.  In response to consumer complaints, samples have been submitted for over 5000 wells in South Carolina.  For 1997 and results to date this year, the data are comparable.  Approximately 35% of the initial samples are positive for total coliform bacteria contamination, an indicator of potential downward leakage of surface contaminants.  Approximately 27% of these samples were confirmed as having fecal coliform bacteria, indicating the presence of contaminated groundwater and the possible presence of pathogens.

DETERMINATION OF COSTS AND BENEFITS:

Internal Costs: Implementation of this regulation will require no additional resources beyond those already being expended.

External Costs: The permit fees for  individual residential wells and irrigation wells are to  be established in  Regulation 61-30.  The fee will provide for inspectors to ensure that individual residential wells and irrigation wells are permitted, inspected on a random basis for proper construction, sampled and analyzed for microbiological parameters as necessary, with enforcement actions were appropriate.

UNCERTAINTIES OF ESTIMATES:	There are minimal uncertainties with regard to internal and external costs.

EFFECT ON ENVIRONMENT AND PUBLIC HEALTH:  The requirements  of  Regulation 61-44 will have a positive effect on human health and the environment through provision of permitting and inspection of individual residential wells to help insure proper construction.

DETRIMENTAL EFFECT ON THE ENVIRONMENT AND PUBLIC HEALTH IF THE REGULATION IS NOT IMPLEMENTED:   An unacceptable  percentage of individual residential wells and irrigation wells will continue to be poorly constructed, thereby increasing the risk to the residents health and increasing the risk of contamination reaching the aquifer(s) being penetrated.